Table of correlated SCPI and API commands on Red Pitaya (date: 21.1.2015)

SCPI	OPTIONS	DESCRIPTION	API
STATE commands
*RST		Reset RP to default settings.	rp_ScpiReset
*IDN? / Example: / *IDN? / Query return: / RedPitaya,EDU_v1.1,00:23:31:45:03:34	<manufacturer>={Red Pitaya} / <model>={EDU_v1.1} / <MAC> = Red Pitaya address	Returns current device information.	rp_ScpiGetID
*SRE? / Query return: / {0xXX, ERR}	http://www.av.it.pt/medidas/data/Manuais%20&%20Tutoriais/40b%20-%20VNA%20-%20ZVB20/CD/documents/Help_Files/WebHelp_ZVA/Remote_Control/Status_Reporting_System/status_registers.htm	Returns STATE BYTE / PON - Bit is always set / URQ - Bit is set when parser get command from user / CME - Bit is set if a command which is undefined or syntactically incorrect is received. / EXE - Bit is set if a received command is syntactically correct, but cannot be performed for other reasons / DDE - Bit is always 0 / QYE - Bit is always 0 / RQC - Bit is set when / OPC - Bit is set on receipt of the command *OPC after all previous commands have been executed. / Register is cleared after reading it!	rp_ScpiGetSRE
*CLS		Delete OPC and EXE bit in SRE	rp_ScpiCls
*OPC		Set OPC bit in SRE / after all previous commands have been executed.	rp_ScpiOpc
*OPC? / Query return: / {0,1, ERR}		Returns OPC bit / 0-operation in process / 1-all operations complete	rp_ScpiGet
LED diodes and GPIOs Red Pitaya
DIG:PIN:DIR <dir>,<pin> / Examples: / DIG:PIN:DIR OUTP,DIO0_N / DIG:PIN:DIR INP,DIO1_P	<dir> = {OUTP,INP} / <pin>={DIO1_P...DIO7_P, DIO0_N...DIO7_N} / OUTP = OUTPUT / IN = INPUT / Default: OUTP	Set direction of digital pins to output or input.	rp_DpinSetDirection
DIG:PIN <pin>,<state> / Examples: / DIG:PIN DIO0_N,1 / DIG:PIN LED2,1	<pin>={DIO1_P...DIO7_P, DIO0_N...DIO7_N, LED1...LED8} / <state>={0,1} / Default: 0	Set state of digital outputs to 1(HIGH) or 0(LOW).	rp_DpinSetState
DIG:PIN? <pin> / Examples: / DIG:PIN? DIO0_N / DIG:PIN? LED2 / Query return: / {0, 1, ERR}	<pin>={DIO1_P...DIO7_P, DIO0_N...DIO7_N, LED1...LED8}	Get state of digital inputs and outputs.	rp_DpinGetState
Analog Inputs and Outputs
ANALOG:PIN <pin>,<value> / Examples: / ANALOG:PIN AOUT0,1 / ANALOG:PIN AOUT2,1.34	<pin>={AOUT0, AOUT1, AOUT2, AOUT3} / <value>={value in Volts} / Default: 0	Set analog voltage on / slow analog outputs. / Voltage range of slow analog outputs is: / 0 -1.8 V	rp_ApinSetValue
ANALOG:PIN? <pin> / Examples: / ANALOG:PIN? AOUT0 / ANALOG:PIN? AIN2 / Query return: / {value in Volts, ERR}	<pin>={AIN0, AIN1, AIN2, AIN3, AOUT0, AOUT1, AOUT2, AOUT3}	Read analog voltage / from slow analog inputs. / Voltage range of slow analog inputs is: / 0 -3.3 V	rp_ApinGetValue
Signal Generator / <n> = {1,2} (set channel OUT1 or OUT2)
OUTPUT<n>:STATE <par> / Examples: / OUTPUT1:STATE ON / OUTPUT2:STATE OFF	<par>={ON,OFF} / Default: OFF	Disable or enable fast analog outputs.	rp_GenOutEnable / rp_GenOutDisable
SOUR<n>:FREQ:FIX <value> / Examples: / SOUR1:FREQ:FIX 1000 / SOUR2:FREQ:FIX 100000	<value>={frequency in Hz} / Default: 1000	Set frequency of fast analog outputs.	rp_GenFreq
SOUR<n>:FUNC <par> / Examples: / SOUR1:FUNC SINE / SOUR2:FUNC TRIANGLE	<par>={SINE, SQUARE, TRIANGLE, SAWU, SAWD PWM, ARBITRARY} / Default: SINE	Set waveform of fast analog outputs.	rp_GenWaveform
SOUR<n>:VOLT <value> / Examples: / SOUR1:VOLT 1 / SOUR2:VOLT 0.5	<value>={voltage in V} / Default: 1 / AMP+OFFS <= |1|V	Set amplitude voltage of fast analog outputs. Amplitude + offset value must be less than maximum output range +/- 1V	rp_GenAmp
SOUR<n>:VOLT:OFFS <value> / Examples: / SOUR1:VOLT:OFFS 0.2 / SOUR1:VOLT:OFFS 0.1	<value>={voltage in V} / Default: 0 / AMP+OFFS <= |1|V	Set offset voltage of fast analog outputs. Amplitude + offset value must be less than maximum output range +/- 1V	rp_GenOffset
SOUR<n>:PHAS <value> / Examples: / SOUR2:PHAS 30	<value>={phase shift in deg} / Default: 0	Set phase of fast analog outputs.	rp_GenPhase
SOUR<n>:DCYC <par> / Examples: / SOUR1:DCYC 34 / SOUR2:DCYC 50	<value>={duty cycle 0-100} / Default: 50 / Only for PWM	Set duty cycle of PWM waveform.	rp_GenDutyCycle
SOUR<n>:TRAC:DATA:DATA <array> / Examples: / SOUR1:TRAC:DATA:DATA 1,0.5,0.2	<array>={value1, value2,...valueN} / max. 16k values / Values are floats in range from -1 to 1.	Import data for arbitrary waveform generation.	rp_GenArbWaveform
SOUR<n>:BURS:STAT <par> / Examples: / SOUR1:BURS:STAT ON / SOUR1:BURS:STAT OFF	<par>={ON,OFF} / Default: OFF	Enable or disable / burst (pulse) mode. / Red Pitaya will generate N period of signal and then stop..	rp_GenMode
SOUR<n>:BURS:NCYC <value> / Examples: / SOUR1:BURS:NCYC 1	<value>={number of burst cycles} / Currently is 1	Set N number of periods for burst mode. Currently N is 1.	rp_GenBurstCount
SOUR<n>:TRIG:SOUR <par> / Examples: / SOUR1:TRIG:SOUR EXT	<par>={EXT_PE,EXT_NE,INT} / EXT = External / INT = Internal / Default: INT	Set trigger source for selected signal.	rp_GenTriggerSource

SOUR<n>:TRIG:IMM / Examples: / SOUR1:TRIG:IMM		Triggers selected source immediately	rp_GenTrigger
TRIG:IMM / Examples: / TRIG:IMM	Mask determines channel: 1->ch1, 2->ch2, 3->ch1&ch2	Triggers both sources immediately	rp_GenTrigger
GEN:RST / Examples: / GEN:RST		Reset generator to default settings.
Acquire / <n> = {1,2} (set channel IN1 or IN2)
Control
ACQ:START / Examples: / ACQ:START		Starts acquisition.	rp_AcqStart
ACQ:RST / Examples: / ACQ:STOP		Stops acquisition and sets all parameters to default values.	rp_AcqReset
Sampling rate & decimation
ACQ:DEC <par>	<par>={1,8,64,1024,8192,65536} / Default: 1	Set decimation factor.	rp_AcqSetDecimation
ACQ:DEC? / Example: / ACQ:DEC? / Query return: / {1,8,64,1024,8192,65536}		Get decimation factor.	rp_AcqGetDecimation
ACQ:SRAT <par>	<par>={125MHz,15_6MHz, 1_9MHz,103_8kHz, 15_2kHz, 1_9kHz} / Default: 125MHz	Set sampling rate.	rp_AcqSetSamplingRate
ACQ:SRAT? / Example: / ACQ:SRAT? / Query return: / {125MHz,15_6MHz, 1_9MHz,103_8kHz, 15_2kHz, 1_9kHz}		Get sampling rate.	rp_AcqGetSamplingRate
ACQ:SRA:HZ? / Example: / ACQ:SRA:HZ? / Query return: / 125000000 Hz		Get sampling rate in Hz.	rp_AcqGetSamplingRateHz
ACQ:AVG <par>	<par>={OFF,ON} / Default: ON	Enable/disable averaging.	rp_AcqSetAveraging
ACQ:AVG? / Example: / ACQ:AVG? / Query return: / {OFF,ON}		Get averaging status.	rp_AcqGetAveraging
Trigger
ACQ:TRIG <par> / Example: / ACQ:TRIG CH1_PE	<par>={DISABLED,NOW,CH1_PE,CH1_NE,CH1_PE,CH1_NE,EXT_PE,EXT_NE,AWG_PE} / Default: DISABLED	Disable triggering, trigger immediately or set trigger source & edge.	rp_AcqSetTriggerSrc
ACQ:TRIG:STAT? / Example: / ACQ:TRIG:STAT? / Query return: / {WAIT,TD}		Get trigger status.	rp_AcqGetTrigger / if DISABLED -> TD / else WAIT
ACQ:TRIG:DLY <par> / Example: / ACQ:TRIG:DLY 2314	<par>={value in samples} / Default: 0	Set trigger delay in samples.	rp_AcqSetTriggerDelay
ACQ:TRIG:DLY? / Example: / ACQ:TRIG:DLY? / Query return: / 2314		Get trigger delay in samples.	rp_AcqGetTriggerDelay
ACQ:TRIG:DLY:NS <par> / Example: / ACQ:TRIG:DLY:NS 128	<par>={value in ns} / Default: 0	Set trigger delay in ns.	rp_AcqSetTriggerDelayNs
ACQ:TRIG:DLY:NS? / Example: / ACQ:TRIG:DLY:NS? / Query return: / 128 ns		Get trigger delay in ns.	rp_AcqGetTriggerDelayNs
ACQ:SOUR<n>:GAIN <par> / Example: / ACQ:SOUR1:GAIN LV	<par>={LV,HV} / Default: LV	Set gain settings to HIGH or LOW. This gain is referring to jumper settings on Red Pitaya fast analog inputs.	rp_AcqSetGain
ACQ:TRIG:LEV <par> / Example: / ACQ:TRIG:LEV 125 mV	<par>={value in mV} / Default: 0	Set trigger level in mV.	rp_AcqSetChannelThreshold / (tu se popravi ime)
ACQ:TRIG:LEV? / Example: / ACQ:TRIG:LEV? / Query return: / 123 mV		Get trigger level in mV.	rp_AcqGetChannelThreshold / (tu se popravi ime)
Data pointers
ACQ:WPOS? / Example: / ACQ:WPOS? / Query return: / {write pointer position}		Returns current position of write pointer.	rp_AcqGetWritePointer
ACQ:TPOS? / Example: / ACQ:TPOS? / Query return: / 1234		Returns position where trigger event appeared.	rp_AcqGetWritePointerAtTrig
Data read
ACQ:DATA:UNITS <PAR> / Example: / ACQ:GET:DATA:UNITS RAW	<par>={RAW, VOLTS} / Default: VOLTS	Selects units in which acquired data will be returned.	rp_AcqScpiDataUnits
ACQ:DATA:FORMAT <PAR> / Example: / ACQ:GET:DATA:FORMAT ASCII	<par>={FLOAT, ASCII} / Default: FLOAT	Selects format acquired data will be returned.	rp_AcqScpiDataFormat
ACQ:SOUR<n>:DATA:STA:END? <start_pos>,<end_pos> / Example: / ACQ:SOUR1:GET:DATA 10,13 / Query return: / {123,231,-231}	<start_pos> ={0,1,...,16384} / <stop_pos> ={0,1,...16384} / stop_pos > start_pos	Read samples from start to stop position.	rp_AcqGetDataPosRaw / rp_AcqGetDataPosV
ACQ:SOUR<n>:DATA:STA:N? <start_pos>,<m> / Example: / ACQ:SOUR1:DATA? 10,3 / Query return: / {1.2,3.2,-1.2}		Read m samples from start position on.	rp_AcqGetDataRaw / rp_AcqGetDataV
ACQ:SOUR<n>:DATA? / Example: / ACQ:SOUR2:DATA? / Query return: / {1.2,3.2,...,-1.2}		Read full buf. size starting from oldest sample in buffer (this is first sample after trigger delay). Trigger delay by default is set to zero (in samples or in seconds). If trigger delay is set to zero it will read full buf. size starting from trigger.	rp_AcqGetOldestDataRaw / rp_AcqGetOldestDataV / size=buf_size !
ACQ:SOUR<n>:DATA:OLD:N? <m> / Example: / ACQ:SOUR2:DATA:OLD? 3 / Query return: / {1.2,3.2,-1.2}		Read m samples after trigger delay, starting from oldest sample in buffer (this is first sample after trigger delay). Trigger delay by default is set to zero (in samples or in seconds). If trigger delay is set to zero it will read m samples starting from trigger.	rp_AcqGetOldestDataRaw / rp_AcqGetOldestDataV
ACQ:SOUR<n>:DATA:LAT:N? <m> / Example: / ACQ:SOUR1:DATA:LAT? 3 / Query return: / {1.2,3.2,-1.2}		Read m samples before trigger delay. Trigger delay by default is set to zero (in samples or in seconds). If trigger delay is set to zero it will read m samples before trigger	rp_AcqGetLatestDataRaw / rp_Ac qGetLatestDataV

ACQ:BUF:SIZE? / Example: / ACQ:BUF:SIZE? / Query return: / 16384		Returns buffer size.	rp_AcqGetBufSize
Oscilloscope TBD!!! / <n> = {1,2} (set channel IN1 or IN2)
RUN / Examples: / RUN		Start Acquisition in Auto and Normal mode.	rp_AcqStart
STOP / Examples: / STOP		Stop Acquisition in all modes (Auto, Normal, Single)	rp_AcqStop
SING / Examples: / SING		In single trigger mode, the acquisition triggers once the trigger conditions are met and then stops. / Once buffer is full acq. stops.	rp_AcqSingle
TFOR / Examples: / TFOR		In single trigger mode, using the TFOR command can generate a trigger signal / forcefully. Once buffer is full acq. stops.	rp_TrigForce
Acquire
ACQ:SRAT <par> / Example: / ACQ:SRAT 125MHz	<par>={125MHz,15_6MHz, 1_9MHz,103_8kHz, 15_2kHz, 1_9kHz}		rp_AcqSetSamplingRate
ACQ:SRAT? / Example: / ACQ:SRAT? / Query return: / {sampling rate Hz, ERR}		Returns sampling rate in Hz	rp_AcqGetSamplingRate
ACQ:AVER <par> / Example: / ACQ:AVER 1024	<par>={1, 8, 64, 1024, 8192, 65535}		rp_AcqSetDecimation
ACQ:TYPE <par> / Example: / ACQ:TYPE AVER	<par>={NORM, AVER}		rp_AcqSetAveraging
Trigger
TRIG:SWE <par> / Example: / TRIG:SWE AUTO	<par>={AUTO, NORM, SING}		rp_SetTriggerMode
TRIG:EDG:SOUR <par> / Example: / TRIG:EDG:SOUR CHAN2	<par>={CHAN1, CHAN2, EXT, AWG}		rp_SetTriggerSrc
TRIG:EDG:SLOP / Example: / TRIG:EDG:SLOP POS	<par>={POS, NEG}		rp_SetTriggerSlope
TRIG:EDG:LEV <value> / Example: / TRIG:EDG:LEV 0.1	<value>={value in mV}		rp_SetTriggerLevel
TRIG:STAT? / Example: / TRIG:STAT? / Query return: / {WAIT, RUN, AUTO, STOP, ERR}	WAIT=WAITING / RUN=RUNNING / STOP=STOPPED	WAIT - signal was not acq. yet, still waiting for trigger event (only in NORM, SING mode) / RUN - acq. was triggered (only in NORM, SING mode) / AUTO - trigger is running in AUTO mode / STOP - acq. is stopped / signal was acquired	rp_GetTriggerStatus
Timebase
TIM:SCAL <par> / Example: / TIM:SCAL: 500ns	<par>={ https://docs.google.com/spreadsheets/d/1dxKMp6AV7hCnR_oLrRAtngvsK-BXKahhsQNdVDzj7wU/edit#gid=0 / }
TIM:DEL:OFFS <value> / Example: / TIM:DEL:OFFS 0.001 mS	<value>={value in seconds} / <value> = f(SRAT) / <value> ={0.000065 [1] , 0.00052 [8], 0.0041 [64], 0.067 [1024], 0.53 [8192], 4.2949 [65535]}	(Aljoša preveri ali SCPI parser omogoča izbiro časovnih enot) / <value> je odvisen od SRAT.	rp_SetTimeDelayOffset
TIM:DEL:OFFS? / Query return: / TIM:DEL:OFFS 0.001 mS			rp_GetTimeDelayOffset
Wavefrom data
WAV:SOUR <par> / Example: / WAV:SOUR CHAN1	<par>={CHAN1, CHAN2}		rp_SetWaveformSource
WAV:FORM <par> / Example: / WAV:FORM FLOAT	<par>={WORD, ASC}	FLOAT-float 32bit binary format in Volts / ASC-float in Volts	rp_SetWaveformFormat
WAV:POIN <value> / Example: / WAV:POIN 1002	<value>={1-16384}	Number of points to be read	rp_SetWaveformPoints
WAV:DATA? / Example: / WAV:DATA? / Query return: / {1.00, 2.00, 1.22}			rp_GetWaveform
WAV:TRIG:SAMP? / Query return: / {0-16383}			rp_GetWaveformTrigSample

rp_ScpiReset
rp_ScpiGetID
rp_ScpiGetSRE
rp_ScpiCls
rp_ScpiOpc
rp_ScpiGet
LED diodes and GPIOs Red Pitaya
rp_DpinSetDirection
rp_DpinSetState
rp_DpinGetState
Analog Inputs and Outputs
rp_ApinSetValue
rp_ApinGetValue
Signal Generator
rp_GenOutEnable / rp_GenOutDisable
rp_GenFreq
rp_GenWaveform
rp_GenAmp
rp_GenOffset
rp_GenPhase
rp_GenDutyCycle
rp_GenArbWaveform
rp_GenMode
rp_GenBurstCount
rp_GenTriggerSource
rp_GenTrigger
rp_GenTrigger
Acquire
Control
rp_AcqStart()
rp_AcqStop()
rp_AcqSingle()
rp_TrigForce()
Acquire
rp_AcqSetSamplingRate(rp_acq_sampling_rate sampling_rate);
rp_AcqGetSamplingRate(float * sampling_rate);
rp_AcqSetDecimation(float * sampling_rate);
rp_AcqSetAveraging(ON|OFF);
Trigger
rp_SetTriggerMode(rp_trg_mode_t mode);
rp_SetTriggerSrc(rp_trig_src_t src);
rp_SetTriggerSlope(rp_trig_slope_t slope);
rp_SetTriggerLevel(float level);
rp_GetTriggerStatus(rp_trig_stat_t * stat);
Timebase

rp_SetTimeDelayOffset(float offset);
rp_GetTimeDelayOffset(float offset);
Wavefrom data
rp_SetWaveformSource(rp_ain_t src);
rp_SetWaveformFormat(rp_wformat_t format);
rp_SetWaveformPoints(int points);
rp_GetWaveform(float * data);
rp_GetWaveformTrigSample(int * value);